## Slide 1: Techniques for Supressing Grating Lobes
Walt Deyzel
21750793
Supervisor Mr. Lanche Grootboom

## Slide 2: Introduction
Antennas are designed to radiate Electromagnetic energy.
It is used for long-distance communication and transmitting of data.

## Slide 3
MeerKAT radio telescope array
located in the Northern Cape
National Radio Astronomy Observatory located west of Socorro, New Mexico

## Slide 5
In the simplest form, an antenna can be modelled as a point source radiating in all directions at a particular frequency. These point source antennas are known as omnidirectional antennas.
Point source antenna
Wavelength:
λ
Speed of light:
c
c = f λ
Operating frequency: f

## Slide 6
The antennas can be arranged in a Linear Antenna Array (LAA).
This improves the overall power gain and improves the directivity.
This means the electromagnetic energy can be transmitted further and more effectively.
Deconstructive Interference
Constructive Interference
k λ

## Slide 7: Problem Statement
This project investigated how the
Position of each antenna element.
phase shift of the signal of each antenna element.
amplitude of the signal of each antenna element.
In an antenna array affect grating lobes and how these parameters should be optimized to suppress the grating lobes while beam steering.

## Slide 8: Objective
The aim is to find a fixed element spacing and the resulting phase shift and amplitude distribution for the LAA that allow for the suppression of grating lobes.
Relative to a uniform LAA of half a wavelength.
These parameters will be obtained by deploying a Genetic Algorithm.
Grating lobes must be suppressed while keeping an acceptable HPBW and SLL.

## Slide 9: Array Factor (AF)
Number of antennas: N
Altering allows for beam steering.
Note
Therefore or
This is knows as the visible region

## Slide 10: Fourier Transform and the AF

## Slide 11: Grating Lobes
Grating lobes are unwanted secondary main lobes.
They are wasted energy and decrease the efficiency of the antenna array.
No grating lobes
Two grating lobes
Four grating lobes.
At and
At , ,and

## Slide 12: Phased Arrays: Steering

## Slide 13: Array Geometry
Uniform LAA
Symmetrical around the mean
Non-uniform
d
d
d
d
d

## Slide 14: Genetic Algorithm
While current generation != maximum generations
  Assign a fitness/error score to each solution.
  Select solutions from the population.
    Tournament selection method.
  Generate offspring (new solution).
    Crossover and Mutation techniques.
  Next generation.
    Immediately copy over fittest solution from the previous generation.
Generate a population of N random solutions.

## Slide 15: Fitness Score
Directivity function
Fitness function

## Slide 16: Uniform LAA

## Slide 17: Using the GA for beam steering
GA: 7.75% fitter
GA: 1.42% fitter
GA: 0.36% fitter
GA: 0.005% less fit

## Slide 18: Optimizing Amplitude distribution.
Antenna elements are spaced 1 wavelength apart. 21.21 dB (159.59%)
Grating lobes are note suppressed when altering the amplitude of the signal entering each antenna elements.
As predicted the amplitude distribution affects the size of the HPBW.
Distribution | SLL (dB)
Uniform | -13.29
Dolph-Chebyshev | -30
Binomial | -55
GA | -35.3

## Slide 19: Non-Uniform spaced LAA vs Uniform LAA

## Slide 20: Non-Uniform spaced LAA vs Uniform LAA

## Slide 21: Results
 | SLL (dB) | HPBW | Directivity
 | SLL (dB) | HPBW | Directivity
Solution 1 vs Uniform LAA
There is a trade off between the SLL, HPBW and directivity.
Uniform LAA | Non-uniform LAA
or 63% of the visible region | ( or (63%-100%) of the visible region This depends on the application.
Uniform LAA | Non-uniform LAA
Steering range

## Slide 22: Conclusion
Grating lobes are as a result of the periodicity of the AF. Only the arrangement in the LAA affect GL.
The GA optimised the LAA for .
The averaging spacing must be smaller or equal to half a wavelength.
A narrower spacing has a larger HPBW but a lower SLL and visa versa.
The amplitude distribution affects lowers the SLL and can increase the HPBW.
The parameters depends on the specifications of the application.